## Slide 1
PS-1 Report
Goa Shipyard Ltd.
Presentation By:
BHANU PARIHAR
GIRIK ROUTARAY
VAIBHAV DEVNANI

## Slide 2
ABOUT GSL
  ISO 9001:2015 for Quality Management Systems (QMS), ISO 14001:2015 for Environment Management Systems, and ISO 45001:2018 for Occupational Health & Safety Management Systems
  operates under the administrative control of the Ministry of Defence, Government of India
  strategically located on the banks of river Zuari in Vasco Da Gama, Goa, a major international tourist destination well connected by its international airport and major port en route to all important shipping lines
  excels in designing and constructing modern patrol vessels with Steel and Aluminium hull structures

## Slide 3
HISTORY
1957: Colonial government of Portuguese India established "Estaleiros Navais de Goa" shipyard to construct barges for the flourishing mining industry in Goa
1961: Military annexation of Goa takes place, shipyard falls into Indian hands, now requisitioned to build warships for the Indian Navy and the Indian Coast Guard
  in-house design capabilities
  caters to both defense and commercial sector
  Patrols vehicles ranging from 29m to 110m

## Slide 4
THE MODERNISATION PROJECT
  4 phased plan includes:
    integrated steel fabrication facility
    dedicated building berths with shiplift and transfer systems
    improved material handling capabilities
    advanced crane facilities
  GSL seeks to achieve high-quality vessel production, cost competitiveness, shorter construction timelines, faster deliveries, increased capacity, and a diversified product portfolio
  based on a "product center concept." - streamlines the ship construction process by establishing four distinct multi-functional production complexes, each equipped for a specific stage of production
  minimizing workforce movement within the shipyard, optimizing equipment and tooling efficiency,creating a highly productive work environment while reducing capital investment and operating costs

## Slide 5
THE MODERNISATION PROJECT
  Phases 1 and 2 of the Modernization Project were commissioned on May 21st, 2011
  capable of docking 120-meter vessels weighing up to 6,000 tons
  Ship Transfer Area spanning approximately 13,600 square meters
  India's first defense shipyard equipped with a modern shiplift facility for launching and docking ships
Upon completion of the project it is expected that:
  Shipyard's capacity for fabricating steel, aluminum, and GRP hull vessels will nearly triple
  ship repair segment will experience a substantial increase

## Slide 6
STRENGTHS
  ISO 9001:2015 certified
  world-class CAD/CAM facility utilizing the Tribon
  ERP-enabled management system integrated with design and planning applications, facilitating effective database management, project monitoring, and control
  state-of-the-art Shift Lift facility capable of accommodating vessels weighing up to 6000 tonnes
  modern steel preparation shop equipped with
    CNC plate-cutting machines
    automatic shot blasting equipment
    CNC pipe bending machine
  modern electronic workshop
  skilled workforce of over 1700 personnel, including a team of more than 265 qualified engineers and naval architects

## Slide 7
SERVICES OFFERED
  vessel design and construction
  simulated training facilities
  vessel repair and modernization
  supply of stern gear
  in-house design facility

## Slide 8
ORGANIZATION CHART

## Slide 9
OUTFITTING DEPARTMENT
  The outfitting engineering department deals with installation of machinery on the ship, their inspection, conducting trials and commissioning.
  Some of the various machineries that are installed are
    Main engine
    Gear Box
    Shaft Generators
    Bow Thrusters
    Diesel generators
    Fuel oil separator
    Propeller
    Fresh water generator
    Fin stabilizer
    Air compressor

## Slide 10
PROPULSION SYSTEM
  Responsible for providing necessary power for movement of the vessel
  3 important parts:
    Engine
    Shafting
    Propeller
  Engine:
    Serves as power source for propulsion system
    traditionally diesel or gasoline IC engine
    alternatively, can be gas turbines, steam turbines or electric motor
    rotational energy generated, transferred to propellers via shafting

## Slide 11
PROPULSION SYSTEM
  Shafting:
    mechanical arrangement of shafts, couples and bearings
    transfers power from engine to propeller
    primary shaft runs from output shaft of engine through hull towards propeller
    sometimes assisted via intermediate shaft for support
  Propeller:
    Converts rotational energy into thrust
    blades attached to a hub
    blades push water to generate thrust
    adjustable blades to control various functions and optimize running
  Together these three systems work together so that ship can run smoothly.

## Slide 12
ENGINES
  Engines can be mainly divided into 3 types:
    Reciprocating Engines
      Diesel
      Gasoline
      Steam
    Turbine Engines
      LNG
      Kerosene/Marine Diesel
      Steam
      Nuclear-powered steam
    Electric Motor
      Purely electric (Batteries)
      Hydrogen Fuel Cell
      Azipods paired with DGs

## Slide 13
The shafting system is a vital component in ship propulsion, responsible for transmitting power from the engine to the propeller. It consists of the shafts, bearing, stern tubes, hydraulic lines for CPP, bearings and couplings.
SHAFTING

## Slide 14
• Shafts
• Bearings
• Couplings
• Sterntube
• Hydraulic system
MAIN COMPONENTS OF THE SYSTEM

## Slide 15
By Location:
  Intermediate Shaft
  Stern/Tail Shaft
  Propellor Shaft
By Construction:
  Hollow Shaft
  Solid Shaft
TYPES OF SHAFTS

## Slide 16
Pre-Launch:
  Pre Inspection
  Initial Installation
  Bearing Alignment
  Coupling Alignment
  Fine Tuning
Post-Launch:
  Re-Alignment
  Monitoring
SHAFT ALIGNMENT

## Slide 17
A Controllable pitch propeller enables a vessel to operate with maximum fuel efficiency, making it energy-saving, environmentally friendly and economical.
The thrust of a vessel can simply be changed by changing the angle of attack of the propeller blades rather than changing the rpm of the engine, this prevents wasting the engines energy and making the vessel more efficient.
CONTROLLABLE PITCH PROPELLER

## Slide 18
• Hub
• Power pack
• Oil distribution box
• Controllable pitch blades
• Hydraulic system
COMPONENTS OF A
CONTROLLABLE PITCH
PROPELLER

## Slide 19
WORKING PRINCIPLE
When the signal is received a spool valve is activated which is in-turn connected to a hydraulic oil pump
A servo motor pushes the hydraulic oil through the pipes inside the hollow shaft.

## Slide 20
The hydraulic oil pushes a piston inside the hub of the propeller blades.
This piston causes the blades to change pitch using the mechanism shown in the diagram
The controllable pitch propeller system also consists of a feedback system. The pump/servo keeps pushing oil until the feedback signal matches the demand signal

## Slide 21
SEA CHEST AND SEA TUBES
Sea Chest
-a chamber located inside the hull of a ship that can be flooded for the intake of water.
Sea Pipes
-responsible for intake of water from the sea chest via pumps.
-provide for various functions inside the ship.
Both are attached with grates to remove debris and organisms
before entering the ship's systems.

## Slide 22
APPLICATIONS
  Engine Cooling
    circulated through heat exchangers to cool down the engine
    maintain optimal temp
  Machinery Cooling
    cooling of other machinery such as pumps, generators, compressors, etc.
  Heat Recovery
    can be used to redirect heat to required locations such as boiler feed water
  Firefighting
    pumped quickly to sprinklers and fire hydrant pipes
  Ballast Operations
    helps balance the ship by redistributing weight in ballast tanks

## Slide 23
SEA TUBE INSTALLATION
  Marking
    marks made by referencing diagrams
  Hole cutting
    holes cut as per marks
  Pipe cutting/preparation/flanging
    pipe cut and prepared as per needed length and angles
    flanges added where connections to be made
  Pipe welding
    pipes welded to each other and other parts before ship installation
  Pickling
    Chemically treated and prepared for welding
  Fitup
    test fitted in ship with all parts before permanent weldś
  Complete welding
    Fully welded with the main ship body making airtight seals

## Slide 24
DIFFERENT TYPES OF PIPE WELDS
No Weld Pass Through
Simple Weld
Doubler Weld
Socket Weld

## Slide 25
DIESEL GENERATOR
  reliable and powerful machines that provide a dependable source of electricity in different settings, including industries, construction sites, and remote areas.
  utilize diesel fuel to produce mechanical energy, which is then converted into electrical power
  efficient and robust
  consistent performance, even under heavy loads,
  widely used as backup power solutions
  usually have a long lifespan

## Slide 26
COMPONENTS
  IC Engine
    consumes fuel to generate rotational mechanical energy
    goes through 4 processes- Suction, Compression, Power, Exhaust
    attached to crankshaft
  Alternator
    attached to the other end of the crankshaft
    has inbuilt magnets and conductive copper wiring that rotates
    uses induction to generate electricity
  Fuel System
    responsible for supply of fuel
    includes pump, filter, ventilation pipe, etc needed for fuel flow
  Lubrication System
    helps smoothly run all the various moving parts
    avoids heating up of parts so that temp is maintained optimal

## Slide 27
COMPONENTS
  Voltage Regulator
    maintains stable output voltage and avoids fluctuations
  Cooling System
    runs coolant fluid to maintain optimal operational temp
    generally water
  Exhaust System
    safely channels away toxic fumes released during combustion in the engine
  Starter And Battery System
    helps initially start the diesel motor, similar to a car battery
  Control Panel
    houses controls for all the various parameters like fuel flow, output voltage, start/stop switch, etc.
  Housing/Frame
    covers and protects all the components of the generator in one single shell

## Slide 28
WORKING PRINCIPLE
Diesel generators go through four combustion processes: Suction, Compression, Power, and Exhaust. The cycle of processes causes the generation of rotational mechanical energy. This energy is transferred to a rotor in the alternator via a crankshaft. The alternator houses conductive copper wiring which spins inside a housing of magnets. This generates a voltage that alternates as per the rotation speed of the shaft

## Slide 29
USAGE ON SHIPS
  supplying electrical power to different systems and equipment on the ship, including lighting, navigation systems, communication systems, refrigeration, ventilation, and various machinery.
  provide backup power in case of a main power failure.
  ensure critical systems like emergency lighting, communication, and essential equipment continue to operate during power outages
  in some ships, can also be used for propulsion in case of emergency
  utilized for refrigeration systems on ships to maintain the required temperature in cold storage areas, such as for perishable goods, provisions, and medical supplies.
  provide power for welding and maintenance activities onboard ships needed for repairs and maintenance work.

## Slide 30
PIPE BENDING
  Various systems and machineries in ships require very complex piping involving 100s of pipes to be precisely routed in a very constrained space.
  Required for - Cooling water circulation, fresh water supply, fuel transport, lubrication system, ballast systems, hydraulic systems
  Complex routing requires a lot of joints and bends, joints usually introduce higher costs, failure points and increased manufacturing time so bending is preferred method to go to accomplish complex plumbing.

## Slide 31
  4 commonly used methods
    Rotary Draw Bending
    Compression Bending
    3 point roll bending
    Ram Bending
  Rotary draw bending with 1 axis and 3 axis semi-automatic and automatic CNC machines is mainly done here. With support for pipes up to 60mm.
PIPE BENDING METHODS

## Slide 32
  Thinning - The challenge of maintaining consistent material thickness during pipe bending to prevent structural weakness or failure
  Folding - The challenge of preventing undesirable creases or folds in the pipe wall during bending, which can compromise its integrity.
  Wrinkling - The challenge of avoiding the formation of wrinkles or ripples on the inner or outer surface of the bent pipe, which can affect its functionality or aesthetics.
  Roundness - The challenge of achieving and maintaining the desired circular shape of the pipe after bending, ensuring proper fit and alignment in the intended application.
  Springback - The challenge of accounting for the tendency of the pipe to return partially to its original shape after bending, requiring careful calculation and adjustment to achieve the desired final shape.
CHALLENGES IN PIPE BENDING

## Slide 33
  Proper selection of bending equipment, such as mandrels, dies, and supports, to minimize material deformation.
  Choosing the right bending technique, such as rotary draw bending, mandrel bending, or heat induction bending, depending on the pipe material, size, and application.
  Applying appropriate lubrication or mandrel coatings to reduce friction and improve material flow.
  Using high-quality materials with suitable mechanical properties for bending applications.
  Conducting thorough pre-bending analysis and simulation to identify potential issues and optimize the bending process.
  It is important to note that the specific challenges and their solutions may vary depending on factors such as the pipe material (e.g., steel, aluminum, copper), wall thickness, diameter, and the complexity of the bend.
WAYS TO OVERCOME CHALLENGES

## Slide 34
  Even after overcoming all the challenges of thinning, wrinkling, roundness etc. the challenge of managing springback is crucial for achieving precise and accurate pipe bends. Here are some strategies to address this challenge:
    Over-Bending
    Heat Treatment
    Multiple step bending
    Slow bending
    Material Selection
  Easiest and commonly used method is Over-Bending, which involved bending the pipes a couple extra degrees so that it can achieve required dimension on springback
CHALLENGE OF SPRINGBACK

## Slide 35
  Various analytical techniques have been researched and developed to predict the springback to compensate it with overbending, but most of them don’t offer results of more than 5-7% accuracy due to the large number of factors involved in the process namely:
    Bending Method
      Ram Bending
      Arc Draw Bending
      Three Point Bending
      Die Bending
    Material Properties
      Young's Modulus
      Hardness Coefficient
    Cracks in material
    Wall thickness
PREDICTING SPRINGBACK
  Hardening Method
  Temperature
  Bending Speed
  Lubrication
  Mandrel Type
    Bead Mandrel
    Ball Mandrel
  Die/Mandrel Material
  Coating/Paint on pipes

## Slide 36
  Involvement of all these factors make it very hard to get general analytical solutions, the only way to predict accurately is via FEM simulations.
  In Industrial applications, automatic machines take advantage of feedback mechanisms to use with a linear/quadratic regression model to get accurate predictions for a pipe type.
  Our goal was to develop a solution for the semi automatic machines to calculate the compensation angle in advance to prevent springback.
  The springback angle is almost linearly related to the bending angle and this property can be used to predict the springback angle for compensation.
PREDICTING SPRINGBACK

## Slide 37
Method to determine the springback -
Bend the pipe by about 30-60 degrees and then measure the final angle, and then repeat the process for a couple of times. This data can be used to calculate the empirical formula to calculate the springback angle for each type of pipe.
The formula that would be obtained will be -
BA = C(RA) + SC
Where,
BA = Bending Angle
RA = Required Angle
SC = Springback Constant (5-15)
C = Proportionality Constant (1.025-1.075)
PREDICTING SPRINGBACK

## Slide 38
This formula can be used to get compensation angles and can achieve results upto 2% accuracy, way higher than theoretical methods. And this just requires 2 test values to begin with.
To get even higher accuracy, quadratic correction term can be introduced which can get less than 1% error
BA = C(RA) + SC + SC*RA^2*QC
Where,
BA = Bending Angle
RA = Required Angle
SC = Springback Constant (5-15)
C = Proportionality Constant (1.025-1.075)
QC = Quadratic Constant (0.0001-0.001)
PREDICTING SPRINGBACK

## Slide 39
This can be implemented in an excel spreadsheet to calculate the compensation angle for a specific type of pipe.
PREDICTING SPRINGBACK

## Slide 40
VESSELS WE WORKED ON

## Slide 41
TALWAR CLASS FRIGATES
• guided missile frigates built for the Indian Navy.
• build in collaboration with Russian Yantar shipyard.
• have a stealthy design making them less visible to enemy radar
•They are armed with an array of weapons, including BrahMos supersonic cruise missiles, surface-to-air missiles, anti-ship missiles, torpedoes, and guns.

## Slide 42
SPECIFICATIONS
Disp. 3,850 t (4,240 short tons) standard load [3] 4,035 t (4,448 short tons) full load [4]
Length. 124.8 m (409 ft 5 in)
Beam. 15.2 m (49 ft 10 in)
Draught. 4.2 m (13 ft 9 in)
Speed. 32 knots (59 km/h; 37 mph)
Time. 30 days
Crew. 180 (18 officers)

## Slide 43
INS SHARDUL
• INS Shardul is an amphibious warfare ship of the Indian Navy, also known as landing craft.
• primarily used to transport troops, vehicles and equipment for launching land based attacks.
• the ship has the capability to come very close to land/beaches to deploy troops
• it can carry up to 500 troops, along with their vehicles and supplies.
• it is used extensively to carry out humanitarian missions.

## Slide 44
SPECIFICATIONS
Displacement. 5650 tons
Length. 125 m (410 ft)
Beam. 17.5 m (57 ft)
Draught. 4 m (13 ft)
Propulsion. Kirloskar PA6 STC engines
Speed. 16 kn (30 km/h; 18 mph)
Troops. 500
Crew. 11 officers, 145 sailors

## Slide 45
ICGS SAGAR
•ICGS Sagar is an offshore patrol vessel (OPV) of the Indian Coast Guard. It is part of the Sagar-class OPVs and serves as a versatile platform for maritime security and surveillance operations.
•ICGS Sagar is armed with medium and light machine guns for self-defense and maritime law enforcement purposes.

## Slide 46
SPECIFICATIONS
Displacement. 1,800 t (1,800 long tons)
Length. 102 m (334 ft 8 in)
Beam. 11.5 m (37 ft 9 in)
Draught. 3.4 m (11 ft 2 in)
Propulsion. 2 x SEMT Pielstick 16 PA6V280 (4,707 kW or 6,312 hp each) diesel engines
Speed. 22 knots (41 km/h; 25 mph)
Complement. 15 officers and 113 sailors

## Slide 47
ARMY FAST PATROL BOATS
• the fast patrol boats will be commitioned by the Indian Army in high altitude regions of Leh and Ladakh
• they have a operating speed of 35 to 40 knots and are armed with two heavy machine guns.
• these fast patrol vessels are being manufactured using futuristic manufacturing methods and are made of mould based fibre.

## Slide 48
SPECIFICATIONS
Length : 35 m
Maximum speed : 35 to 40 knots
Armaments: 2 heavy machine guns

## Slide 49
THANKYOU